## Slide 1: Trick Simulation Environment: Advanced Topics
John Penn (L-3Com/ER7)
Danny Strauss (L-3Com/ER7)
Alex Lin (NASA/ER7)
also authored by
Scott Killingsworth (NASA/ER7)
Eddie Paddock (NASA/ER7)
Les Quiocho (NASA/ER7)
Keith Vetter (Spoonbill Services/ER7)

## Slide 2: Agenda/Schedule
Realtime and Distributed Topics
  Trickcomm and the Variable Server
  Multiprocessing and Realtime
  Master/Slave Import/Export
  Real World Realtime/Multiprocessing/Master/Slave example
  Monte Carlo
  Generic Malfunction Insertion
  Units Upgrade
  Wide Character Support
Additional Material
  External Clocks and Timers
  External Libraries and Trick Math Library

## Slide 3: Trickcomm and the Variable Server

## Slide 4: Trickcomm and the Variable Server
Objective
  Describe the Trickcomm package
  Describe the Variable server
Prerequisites
  Knowledge of sockets

## Slide 5: Trickcomm
Trickcomm is a C library built on top of the system TCP/IP socket library.
Originally, Trickcomm was provided as a consistent “stream” interface over sockets, reflective memory, and shared memory.
Sockets have proved fast enough so Trickcomm only supports sockets.
Trickcomm can be used as a standalone package.
  Usable as a library to non-Trick sims
  Usable under Windows

## Slide 6: Trickcomm
Provided functions – Connecting (Server)
  tc_init(TCDevice * listen_device) ;
    Initializes a listen socket and begins listening for a client connection.
    listen_device.port must be specified. Uses unix listen().
  tc_listen(TCDevice * listen_device) ;
    Returns true if a client is trying to connect on the listen socket.
    Uses unix poll().
  tc_accept(TCDevice *listen_device, TCDevice *device) ;
    Accepts the client connection request from listen_device onto device.
    Will block until client connects. Endianness of client is recorded.
    Uses unix accept().
Provided function – Connecting (Client)
  tc_connect(TCDevice *device);
    Connects to a listening socket. Endianness of server is recorded.
    listen_device.port & hostname must be specified. Uses unix connect().

## Slide 7: Trickcomm
Provided functions – Connecting (Server and Client)
  tc_multiconnect(TCdevice *device, char *connection_tag, char *my_tag, TrickErroHndlr *error_handler) ;
    Both the server and client call tc_multiconnect
    Each side provides connection_tag which must be equal
    Each side provides my_tag which must be different
    tc_multiconnect will use multicasting sockets to find other connections that have the same connection_tag and different my_tag
    tc_multiconnect will determine who is the server and client and call tc_accept and tc_connect with appropriate port numbers to establish a connection (user does not specify port)
    tc_multiconnect returns when the connection is made
process 1:
tc_multiconnect(dev , “important_comm!” , “side a” , err_hndlr) ;
process 2:
tc_multiconnect(dev , “important_comm!” , “side b” , err_hndlr) ;

## Slide 8: Trickcomm
Provided functions – Read/Write
  tc_read(TCDevice * device, char *buffer, int size) ;
    Reads size number of bytes
  tc_write(TCDevice * device, char *buffer, int size) ;
    Writes size number of bytes
  tc_read_byteswap(TCDevice * device, char *buffer, int size, ATTRIBUTES *attr) ;
    Calls tc_read. If other side of connection is opposite endianness, takes structure information of buffer from attr and byteswaps buffer .
    attr is generated for each structure by ICG (in S_source.c)
  tc_write_byteswap(TCDevice * device, char *buffer, int size, ATTRIBUTES *attr) ;
    If other side of connection is opposite endianness, takes structure information of buffer from attr and byteswaps buffer . Calls tc_write.
    attr is generated for each structure by ICG (in S_source.c)

## Slide 9: Trickcomm - Blocking
Provided Functions - Blocking
  tc_blockio(TCDevice * device, TCCommBlocking blockflag);
    Sets the socket blocking type
    Blocking
      A connection that "blocks" on a read/write will wait until it has read/written all the data over its connection before proceeding. Blocking will force a system call and put itself to sleep and wait on the OS to wake it up.
    No blocking
      "Non-blocking" is asynchronous in nature and will read/write whatever it can offering no guarantee that it has finished.
    Timed blocking
      The timed block will block for a specified period of time, and give up if time expires. The "timed block" will consume CPU time as the read waits for data.
    “All or nothing" blocking
      The "all or nothing" block will not block until there is something to read. Once something is on the pipe, it will block indefinitely until it receives all data it expects. The "all or nothing" approach will consume CPU time as it waits.
  tc_set_blockio_timeout_limit(TCDevice *device, double limit) ;
    Sets the time a Timed blocking socket will wait for data

## Slide 10: Trickcomm
Provided Functions
  tc_pending(TCDevice * device) ;
    Checks to see if any data is available for reading
  tc_isValid(TCDevice * device) ;
    Checks to see if the socket is still connected
  tc_error(TCDevice *device, int on_off) ;
    Turns on/off error messages from trickcomm activity
  tc_disconnect(TCDevice * device) ;
    Disconnects a socket

## Slide 11: Trick Communications
Server
Initialize Listen Device
tc_init(TCDevice * listen_device) ; Server sets up a socket called a "listen device" to listen for client connections. This listen is done on a predetermined port agreed upon by server and client. Returns when a connection is ready to made on the listen device
Accept Client
tc_accept(TCDevice *listen_dev , TCDevice *dev)
Accept client on listen device socket. Returns dev
Setup Blocking
tc_blockio(TCDevice *dev, TCCommBlocking block);
Set the socket to blocking/timed/non blocking/all or nothing
Read and Write
tc_read(TCDevice *dev, char *buffer, int size);
tc_write(TCDevice *dev, char *buffer, int size) ;
Send and receive data
Close Conection
tc_disconnect(TCDevice *dev);
Shutdown the socket
Client
Connect To Server
tc_connect(TCDevice *)
Client connects to server over socket. Connection is done over predetermined port.
Setup Blocking
tc_blockio(TCDevice *dev, TCCommBlocking block);
Set the socket to blocking/timed/non blocking/all or nothing
Close Conection
tc_disconnect(TCDevice *dev);
Shutdown the socket
Read and Write
tc_read(TCDevice *dev, char *buffer, int size);
tc_write(TCDevice *dev, char *buffer, int size) ;
Send and receive data
Server/Client Communication Sequence

## Slide 12: Trick Communications
Server
Connect to other side
tc_multiconnect(TCDevice *, char *t1, char *t2…) ; Finds other machine/port number. Determines who is server/client. Connects and returns device
Setup Blocking
tc_blockio(TCDevice *dev, TCCommBlocking block);
Set the socket to blocking/timed/non blocking/all or nothing
Read and Write
tc_read(TCDevice *dev, char *buffer, int size);
tc_write(TCDevice *dev, char *buffer, int size) ;
Send and receive data
Close Conection
tc_disconnect(TCDevice *dev);
Shutdown the socket
Client
Setup Blocking
tc_blockio(TCDevice *dev, TCCommBlocking block);
Set the socket to blocking/timed/non blocking/all or nothing
Close Conection
tc_disconnect(TCDevice *dev);
Shutdown the socket
Read and Write
tc_read(TCDevice *dev, char *buffer, int size);
tc_write(TCDevice *dev, char *buffer, int size) ;
Send and receive data
Communication Sequence with tc_multiconnect
Connect to other side
tc_multiconnect(TCDevice *, char *t1, char *t2…) ; Finds other machine/port number. Determines who is server/client. Connects and returns device

## Slide 13: Variable Server
What is the variable server?
  The variable server is a TCP/IP server (using Trickcomm) which runs in an asynchronous simulation thread. Clients may connect to the server and set/get simulation parameters.
Why use it?
  Nice for interactive GUIs
  Simple asynchronous way to drive the simulation
  Simple interface for probing states for graphics displays or strip charts
  Useful for crew training when an instructor needs to introduce a specific scenario on-the-fly
  Useful for debugging

## Slide 14: Variable Server
Where to connect?
  Client needs to know the hostname and port
    As of 10.5, a random port number is chosen by the operating system when the simulation is starting.
    The port number may be overridden in the input file.
      trick.var_server_set_port(unsigned short port)
    External applications may listen to the variable server broadcast channel (224.3.14.15 port 9265) to get variable server host information.
      See section 7.xx Variable Server of the User’s guide for information on the format of the broadcast information.

## Slide 15: Variable Server
Variable server sends all commands through Python
  All valid python commands available
    Setting variables with assignment statements (e.g. mystruct.x = 5.0),
    command simulation to run/freeze/dump checkpoint,
    call jobs,
    etc…

## Slide 16: Variable Server
User accessible routines
  These commands may be used in model code to get the status of the variable server.
    const char* var_server_get_hostname()
    int var_server_get_port()
    int var_server_get_enabled()
    int var_server_set_enabled(int on_off)
Note: Disabling the variable server will disable the Trick runtime GUIs.

## Slide 17: Variable Server
In addition to handling all valid python commands, the variable server has specific commands to handle sending back data to the client at a semi-regular frequency
  trick.var_add(string var_name)
    Add a variable name to the list to send back to the client.
  trick.var_add(string var_name, string units)
    Add a variable name to the list to send back to the client with the desired return units.
  trick.var_remove(string var_name)
    Remove a variable name from the list.
  trick.var_send()
    Forces the variable server to return the list of values immediately.
  trick.var_clear()
    Clears the list of variables
  trick.var_cycle(double cycle_rate)
    Sets the frequency of data being sent
  trick.var_pause()
    Pauses variable server from returning data, but it still accepts new commands
  trick.var_unpause()
    Resumes sending the data
  trick.var_exit()
    Disconnects the current client form the variable server

## Slide 18: Variable Server
Other variable server commands
  trick.var_units(string var_name, string units)
    Use the specified units with var_name. If the units are changed, then the units are included in the returned string.
  trick.var_debug(int level)
    Level range from 0-3.
    Print out increasing amounts of debugging information
  trick.var_ascii()
    Sets the message format to ascii (default)
  trick.var_binary()
    Sets the message format to binary
  trick.var_sync(int level)
    When 0, variables are retrieved using an asynchronous thread. The values are not guaranteed to be time homogenous.
    When 1, variables are retrieved by the main thread at the end of it’s frame. Values are time homogenous. Variables are sent to the client using an asynchronous thread.
    When 2, variables are retrieved as they are in level 1. Variables are sent to the client in the main thread.
  trick.var_exists(string var_name)
    To test if a var_name exists.

## Slide 19: Variable Server
Returned Values
  By default, the values are sent asynchronously to the client.
  Values will be returned to the client in the same order that they were issued in the var_add command(s).
  Ascii Format
    The default format which causes the variable server to return a buffer containing a tab delimited character string in the following format:
0\t<variable1 value>\t<variable2 value>{<variable2 units>}\t<variableN value>\n
    The 1st value returned in the list will always be a message indicator. Below are the possible values:
      0 returned variable value(s) from var_add or var_send
      1 returned value from var_exists
        1<1 byte binary 0 or 1>
      2 returned value from send_sie_resource
      -1 input parse error occurred while processing command (NOT IMPLEMENTED)

## Slide 20: Variable Server
  Binary Format
    The variable server will return values in a binary message in the following format:
<message indicator><message size><N>
<var1 name length><var1 name><var1 type><var1 size><var1 value>
<var2 name length><var2 name><var2 type><var2 size><var2 value>
.
.
<varN name length><varN name><varN type><varN size><varN value>
    message indicator: same possible values as the Ascii message : 4 byte integer
    message size: total size of the message in bytes (NOT including message indicator) : 4 byte integer
    N : the number of variables registered via the var_add command : 4 byte integer
    Var name length: the string length of the variable’s name : 4 byte integer
    Var name: the Ascii variable string name : var name length bytes of string
    Var type: Trick data type of the variable : 4 byte integer
    Var size: the number of bytes the variable occupies in memory : 4 byte integer
    Var value: the variable’s current value : var size bytes of var type

## Slide 21: Variable Server
All of Trick’s runtime GUIs use the variable server
  Sim control panel
  Trick View (TV)
  Malfunction Trick View (MTV)
  Stripcharts